## Slide 1: 邊緣人工智慧 Edge AI
(General-Purpose) AI Accelerators
吳凱強
Kai-Chiang Wu

## Slide 2: Outline
Benchmarking Metrics
GEMM Accelerator Design
DNN Accelerator Design
Energy

## Slide 3: How Can We Compare Designs?
Key metrics
  Accuracy
  Throughput
  Latency
  Energy consumption
  Power consumption
  Hardware cost
Importance of each of these metrics
Factors that affect each metric

## Slide 4: Accuracy
Indicate the quality of the result for a given task
  The units used to measure accuracy depend on the task
  Image classification
    Top-1, Top-5 accuracy
  Object detection
    Mean Average Precision (mAP)
Factors that affect accuracy
  Difficulty of the task and dataset
    Object detection or semantic segmentation is more difficult than classification
  Evaluating hardware performance using well-studied, widely used DNN models, tasks, and datasets

## Slide 5: Accuracy
Motivated by the impact of the SPEC benchmarks for general-purpose computing
MLPerf
  Serve as a common set of well-studied DNN models to evaluate hardware performance
  Put together a broad suite of DNN models
    Various types of DNNs
    Various tasks
    Image classification, object detection, semantic segmentation, translation, speech-to-text, recommendation, sentiment analysis, and reinforcement learning
  Enable fair comparison of various software frameworks, hardware accelerators

## Slide 6: Throughput and Latency
Throughput
  Amount of data that can be processed/completed in a given time period
  Reported as
  Applications that action needs to be promptly taken based on the analysis require high throughput
    E.g., Real-time video processing, security, terrorist prevention, medical diagnosis, drug discovery
Latency (response time)
  Real-time interactive applications require low latency
    E.g., AR, autonomous navigation, robotics

## Slide 7: Throughput vs. Latency
Pitfall
  Throughput and latency can be directly derivable from one another
Batching input data
  Increase throughput but increase latency in real-time video processing
  E.g., at 30 frames per second and a batch of 100 frames, some frames will experience at least 3.3 second delay
Real-time navigation requires low latency but can bear low throughput

## Slide 8: Factors that Affect Throughput
Consider a system comprised of multiple processing elements (PEs)
PE – a simple or primitive core that performs a single MAC operation

## Slide 9: Increase Throughput
Increase → higher clock frequency → reducing critical path
  Affected by design of the MAC
Increase 𝑛𝑢𝑚𝑏𝑒𝑟𝑜𝑓 𝑃𝐸𝑠 → multiple MACs perform in parallel
  If Area cost of the system is fixed
    Increasing the area density of the PEs
    Trading off on-chip storage area for more PEs
      Affect the utilization of the PEs
  Increasing the density of PEs
    Reducing the logic associated with delivering operands to a MAC
      Multiple MACs share control logic
      E.g., SIMD and SIMT with CPUs and GPUs

## Slide 10: Increase Throughput
Number of active PEs – number of PEs that receive work
  Distribute the workload to as many PEs as possible
Ability to distribute the workload
  Determined by the flexibility of the architecture
  Network-on-Chip (NoC) matters!

## Slide 11: Increase Throughput
With the constraint of NoC
Number of active PEs
  Determined by the specific allocation of work to PEs by the mapping process
  Involves the placement and scheduling in space and time of every MAC operation onto the PEs
  Mapping a compiler for the DNN hardware
Utilization of the active PEs
  Timely delivery of work to the PEs
  Affected by
    Bandwidth and latency of the memory hierarchy and network
    Imbalance of work allocated across Pes
      Native sparsity often result in lower utilization

## Slide 12: Bandwidth Requirements
Affected by the amount of data reuse available in DNN models
Amount of data reuse can be exploited by the memory hierarchy and dataflow
Dataflow determines the order of operations and where data is stored and reused
E.g., Larger batch size → higher amount of data reuse

## Slide 13: Interplay Between
Reduce the likelihood that a PE needs to wait for data is to store some data locally near or within the PE
  Increasing the chip area of on-chip storage
  Reducing the number of PEs
How to balance areas of PEs and on-chip storage?

## Slide 14: Roofline Model
Design goal: operate as close as possible to the peak operations
per second for the operation intensity of a given workload

## Slide 15: How DNN Models Affect
depends on the DNN model only
depends on both DNN model and hardware
  Efficient DNN models
    Reduce the number of MAC operations → reduce number of operations per inference
    Wide range of layer shapes → Poor utilization of PEs → Reduce the overall operations per second
Number of ineffectual operations is a function of both the DNN model and the input data
  E.g., MAC accumulates anything multiplied by zero → sparsity (ineffectual operation)

## Slide 16: Effectual and Ineffectual Operations
Amount of sparsity increase → increase
  Requires additional hardware → increase critical path, reduce area density of PE → reduce
  Trade off

## Slide 17: Reducing Precision (e.g., Quantization)
Increase
Lower precision (fewer bits) → lower bandwidth requirement → increase utilization of PEs
Multiple levels of precision requires addition hardware → increase critical path, reduce area density of PE → decrease

## Slide 18: Factors that Affect Inferences per Second

## Slide 19: MAC Alone as an Performance Estimation
Measured on Pixel phone
#MACs is not a good predictor of latency …
Design efficient DNN models with hardware in the loop!

## Slide 20: How Can We Compare Designs?
Key metrics
  Accuracy
  Throughput
  Latency
  Energy consumption
  Power consumption
  Hardware cost
Importance of each of these metrics
Factors that affect each metric

## Slide 21: Energy Efficiency and Power Consumption
Energy Efficiency
  Given unit of energy, how much data that can be processed
  Edge processing requires high energy efficiency
Power consumption
  Amount of energy consumed per unit time
  Increase power consumption → increase heat dissipation
  Thermal Design Power (TDP) limits max power consumption

## Slide 22: Relation between Throughput
increasing the → increase → increase throughput

## Slide 23: Factors that Affect Energy Efficiency
: switching activity
: switching capacitance
: supply Voltage

## Slide 24: Energy Consumption
45nm process
Energy consumption is dominated by the data movement
  Capacitance of data movement tends to be much higher than the capacitance for arithmetic operations (PEs)
Larger memories and longer interconnects
  Consume more energy
Optimizing data movement is the key!

## Slide 25: Operations per Joule
A function of the ability of the hardware to exploit sparsity to avoid performing ineffectual MAC operations

## Slide 26: Hardware Cost
Process technology
Amount of on-chip storage and compute → Area
  PEs in DNN accelerator
  Cores in CPU and GPU
  Digital Signal Processing (DSP) Engines in FPGA
Off-chip bandwidth
  Complexity of the packaging
  PCB design
  Off-cihp DRAM, NVLink, etc.

## Slide 27: Flexibility
Range of DNN models and tasks that can be supported on the DNN processor
Ability of the software environment to maximally exploit the capabilities of the hardware
Two aspect of support for different DNN models
  Functionally support
  Maintain efficiency
Different network architectures
Different levels of precision
Different degrees of sparsity
Different types of DNN layers and computation beyond MAC operations

## Slide 28: Scalability
How well a design can be scaled up to achieve higher throughput and energy efficiency
  Size of the Chip
  Multiple chips
  PE, on-chip storage
Usually non-linear when scaling up
  Reduced utilization of PEs
  Increase cost of data movement

## Slide 29: Metrics for DNN Hardware
Accuracy
  Quality of result for a given task
Throughput
  Analytics on high volume data
  Real-time performance (e.g., video at 30 fps)
Latency
  For interactive applications (e.g., autonomous navigation)
Energy and Power
  Edge and embedded devices have limited battery capacity
  Data centers have stringent power ceilings due to cooling costs
Hardware Cost
  Money

## Slide 30: Specifications to Evaluate Metrics
Accuracy
  Difficulty of dataset and/or task should be considered
Throughput
  Number of cores (include utilization along with peak performance)
  Runtime for running specific DNN models
Latency
  Include batch size used in evaluation
Energy and Power
  Power consumption for running specific DNN models
  Include external memory access
Hardware Cost
  On-chip storage, number of cores, chip area + process technology

## Slide 31: Example: Metrics of Eyeriss Chip

## Slide 32: Comprehensive Coverage
All metrics should be reported for fair evaluation of design tradeoffs
Examples of what can happen if certain metric is omitted:
  Without the accuracy given for a specific dataset and task, one could run a simple DNN and claim low power, high throughput, and low cost – however, the processor might not be usable for a meaningful task
  Without reporting the off-chip bandwidth, one could build a processor with only multipliers and claim low cost, high throughput, high accuracy, and low chip power – however, when evaluating system power, the off-chip memory access would be substantial
Are results measured or simulated? On what test data?

## Slide 33: Evaluation Process
The evaluation process for whether a DNN system is a viable solution for a given application might go as follows:
Accuracy determines if it can perform the given task
Latency and throughput determine if it can run fast enough and in real-time
Energy and power consumption will primarily dictate the form factor of the device where the processing can operate
Cost, which is primarily dictated by the chip area, determines how much one would pay for this solution

## Slide 34: Outline
Benchmarking Metrics
GEMM Accelerator Design
  GEMM
  Systolic and Other Variation
DNN Accelerator Design
Energy

## Slide 35: Basic Linear Algebra Subprograms (BLAS)
The building blocks of most of scientific computing
Application codes either call these routines directly, indirectly through other libraries that themselves call the BLAS, or via environments like Matlab
Three Levels:
  Level 1: vector-vector operations
  Level 2: matrix-vector operations
  Level 3: matrix-matrix operations
Implementing level-3 BLAS in terms of GEneral Matrix-Matrix multiplication (GEMM) kernels
  Only a small set of kernels needed to be highly optimized

## Slide 36: Basic Linear Algebra Subprograms (BLAS)

## Slide 37: Why GEMM?
Linear Algebra Package (LAPACK) level
  Matrix factorizations
Basic Linear Algebra Subroutines (BLAS)
  Matrix-matrix and matrix-vector operations
Inner kernels
  Hand-optimized
Accelerators
  optimize GEMM
GEMM is crucial for many critical applications
  Especial for DNNs

## Slide 38: Native GEMM Implementation
Flops = →
Operate on words of memory
Questions
  What is the performance of this code?
  Where is the cause of problem with this code?
  How can we improve it ?
  What is an easy way to increase the performance with minimum code change?

## Slide 39: Recursive GEMM
Divide & conquer
How does it work with non-squared matrices?
Why does it improve performance?

## Slide 40: Blocked GEMM

## Slide 41: GEMM Kernel
Rank-1 update
  Update matrix by adding outer product of two vectors to it
Matrix multiplication as a series of rank-1 updates
  Let C, A, and B be 4 x 4, 4 x kc and kc x 4 matrices
  C+=AB can be computed as: for i = 0 ~ kc -1

## Slide 42: The GEMM Micro-kernel

## Slide 43: The GEMM Micro-kernel
Typical micro-kernel loop iteration
(“block-dot product”)
Load column of packed A
Load row of packed B
Compute outer product
Update C (kept in registers)

## Slide 44: The GEMM Micro-kernel
Why MR x NR block-dot product?
  Why not a simple scalar dot product?
  Ratio of floating-point operations to memory operations

## Slide 45: The GEMM Micro-kernel
BLIS exposes outer two loops of the inner kernel
  Key observation: Virtually all of the differences between level-3 inner kernels reside in the outer two loops (e.g. loop bounds)
  All inner kernels (which we call “macro-kernels”) are provided as part of the BLIS framework (C99)
  Inner-most exposed loop simply calls micro-kernel

## Slide 46: GEMM Loops
Rules for each new character
  Buffers
  Re-fetch rate

## Slide 47: Memory Hierarchy

## Slide 48: Design Hardware for GEMM
Systolic Arrays
  Systolic Arrays
  GEMM Systolic solution
Other
  Other parallel GEMM algorithm

## Slide 49: Outline
Benchmarking Metrics
GEMM Accelerator Design
  GEMM
  Systolic and Other Variation
DNN Accelerator Design
Energy

## Slide 50: Systolic Arrays
Systolic arrays are hardware structures built for fast and efficient operation of regular algorithms that perform the same task with different data at different time instants. Systolic arrays replace a pipeline structure with an array of processing elements that can be programmed to perform a common operation.

## Slide 51: Definitions of Systolic Array
“Imagine n simple processors arranged in a row or an array and connected in such a manner that each processor may exchange information with only its neighbors to the right and left. The processors at either end of the row are used for input and output. Such a machine constitutes the simplest example of a systolic array.”
Bayoumi, M. A., & Ling, N. (1999). Specification and verification of systolic arrays. World Scientific.

## Slide 52: Definitions of Systolic Array
“Systolic Arrays are regular arrays of simple finite state machines, where each finite state machine in the array is identical...A systolic algorithm relies on data from different directions arriving at cells in the array at regular intervals and being combined.”
Brown, Andrew (1991). VLSI Circuits and Systems in Silicon. McGraw-Hill Boo Company.

## Slide 53: Definitions of Systolic Array
“By pipelining, processing may proceed concurrently with input and output, and consequently overall execution time is minimized. Pipelining plus multiprocessing at each stage of a pipeline should lead to the best-possible performance.”
Dewdney, A.K. (1993) The (New) Turing Omnibus. Henry Holt and Company.

## Slide 54: Systolic Arrays
This is a form of pipelining, sometimes in more than one dimension
The term systolic was first used in this context by H.T. Kung, then at CMU; it refers to the “pumping” action of a heart
Machines have been constructed based on this principle, notable the iWARP, fabricated by Intel

## Slide 55: Systolic Arrays
Balancing computation with I/O

## Slide 56: Systolic Architectures
Replace single processor with an array of regular processing elements
Orchestrate data flow for high throughput with less memory access
Different from linear pipelining
  Nonlinear array structure, multidirectional data flow, each PE may have (small) local instruction and data memory
Different from SIMD: each PE may do something different
Initial motivation: VLSI Application-Specific Integrated Circuits (ASICs)
Represent algorithms directly by chips connected in regular pattern

## Slide 57: Systolic Matrix Multiplication
Processors are arranged in a 2-D grid
Each processor accumulates one element of the product
The elements of the matrices to be multiplied are pumped through the array

## Slide 58: Data Preparation for Systolic
We need to modify the input data, like so:

## Slide 59: Systolic Matrix Multiplication
3x3 matrices multiplications
Processors arranged in a 2-D grid
Each processor accumulates one element of the product

## Slide 60: Systolic Matrix Multiplication

## Slide 61: Systolic Matrix Multiplication

## Slide 62: Systolic Matrix Multiplication

## Slide 63: Systolic Matrix Multiplication

## Slide 64: Systolic Matrix Multiplication

## Slide 65: Systolic Matrix Multiplication

## Slide 66: Systolic Matrix Multiplication

## Slide 67: Strips View of Systolic Array
Let’s take another view of systolic multiplication
  Consider the rows and columns of the matrices to be multiplied as strips that are slide past each other.
The strips are staggered so that the correct elements are multiplied at each time step.

## Slide 68: Strips View of Systolic Array

## Slide 69: Strips View of Systolic Array

## Slide 70: Strips View of Systolic Array

## Slide 71: Strips View of Systolic Array

## Slide 72: Strips View of Systolic Array

## Slide 73: Cannon’s Method
Rather than have some processors idle
  wrap the array rows and columns so that every processor is doing something on each step.
In other words, rather than feeding in the elements, they are rotated around
Starting in an initially staggered position as in the systolic model.
We also change the order of products slightly, to make it correspond to more natural storage by rows and columns
Not including the loading which can be done in parallel for a time of 1, this technique is effectively N.

## Slide 74: Cannon Variation

## Slide 75: Application of Cannon’s Technique
Consider matrix multiplication of 2 n x n matrices on a distributed memory machine, on say, n2 processing elements.
An obvious way to compute is to think of the PE’s as a matrix, with each computing one element of the product.
We would send each row of the matrix to n processors and each column to n processors.
In effect, in the obvious way, each matrix is stored a total of n times.

## Slide 76: Obvious Matrix Multiply
Row x Column
on respective PEs
Columns of b distributed
to each PE in column
Rows of a distributed
to each PE in row

## Slide 77: Cannon’s Method
Cannon’s method avoids storing each matrix n times, instead cycling (“piping”) the elements through the PE array.
  It is sometimes called the “pipe-roll” method.
The problem is that this cycling is typically too fine-grain to be useful for element-by-element multiply.

## Slide 78: Block Multiplication

## Slide 79: Cannon’s Method is Fine for Block Multiplication
The blocks are aligned initially as the elements were in our description
At each step, entire blocks are transmitted down and to the left of neighboring PE’s
Memory space is conserved

## Slide 80: Fox’s Algorithm
For block matrix multiplication, it has a resemblance to Cannon’s algorithm.
The difference is that on each cycle:
  A row block is broadcast to every other processor in the row.
  The column blocks are rolled cyclically

## Slide 81: Fox’s Algorithm

## Slide 82: SUMMA Algorithm

## Slide 83: Remarks
Cannon’s algorithms
  Roll-roll-multiply
Fox’s algorithm
  Broadcast-roll-multiply
SUMMA
  Broadcast-broadcast-multiply

## Slide 84: Systolic Array Architectures

## Slide 85: [C] = [A]x[B] Variation
Keep C resident
Stream A,B
Keep A resident
Stream B,C
Keep B resident
Stream A,C

## Slide 86: Systolic Array – Example

## Slide 87: Outline
Benchmarking Metrics
GEMM Accelerator Design
DNN Accelerator Design
  Locality and Data Reuse
  Dataflow Taxonomy
  Network-on-Chip
  Optimization
Energy

## Slide 88: Direct Convolution is Better
Higher performance, zero memory overheads

## Slide 89: Highly-Parallel Compute Paradigms

## Slide 90: Locality: Temporal and Spatial Reuse
Temporal reuse: the same data is used more than once over time by the same consumer.
Spatial reuse: the same data is used by more than one consumer at different spatial locations of the hardware.

## Slide 91: Temporal Reuse
The same data value is used more than once by the same consumer
  E.g. PE
Adding an intermediate memory level to the memory hierarchy
  Used multiple times at the intermediate level
  Reduces the overall energy cost

## Slide 92: 1D CNN Temporal Reuse Example
Example 1D convolution
Operation ordering = 1, reuse distance = 4

## Slide 93: 1D CNN Temporal Reuse Example
Example 1D convolution
Operation ordering = 2, reuse distance = 1

## Slide 94: Temporal Reuse Distance
Temporal reuse distance
  The maximum number of data accesses required by the consumer in between the accesses to the same data value
  Storage capacity of the intermediate memory level limits the maximum reuse distance
  Storage capacity >= maximum reuse distance
      Temporal reuse can be exploited
  Not limit to weights
Reduce the reuse distance of one data type often increase the reuse distance of other data types
Exploited by multiple levels of the memory hierarchy

## Slide 95: Spatial Reuse
The same data value is used by more than one consumer at different spatial locations of the hardware
  E.g., a group of PEs
Exploited by reading the data once from the source memory level and multicasting it to all of the consumers
Reducing the number of accesses to the source memory level
  Reduces the overall energy cost
Reducing the bandwidth required from the source memory level
  Helps to keep the PEs busy and therefore increases performance

## Slide 96: Spatial Reuse Distance
If no storage capacity in a group of consumers
  Spatial reuse can only be exploited by the subset of consumers that can process the data in the same cycle as the multicast of the data
Spatial Reuse Distance
  The maximum number of data accesses in between any pair of consumers that access the same data value

## Slide 97: Memory Hierarchy for Spatial Reuse

## Slide 98: Spatial Reuse Example
Operation ordering = 1,
reuse distance = 0
Operation ordering = 2,
reuse distance = 1
Operation ordering = 3,
reuse distance = 3

## Slide 99: Routing Data to Multiple Destination
Network-on-Chip(NoC)
  Support the data distribution patterns as derived from the ordering of operations
Exploiting spatial reuse at higher levels of the memory hierarchy creates more duplicated data in the hardware
Supporting multicast to all consumers in a single level at a large scale can also be expensive
Trade-off
physical connectivity of the NoC between the L1 memory and the
consumers limits the multicast from any banks in L1 to all consumers

## Slide 100: Reducing Reuse Distance
Data stay stationary over time in the sequence of operations
  Reduce temporal reuse distance
Data tiling (or blocking)
  Temporal tiling
    Reduce temporal reuse distance
    Reducing the reuse distance of specific data types
    Make it smaller than the storage capacity of a certain memory level in the memory hierarchy
  Spatial tiling
    Reduce spatial reuse distance
    Reusing the same data value by as many consumers as possible
    Reducing the reuse distance so that one multicast can serve as many consumers as possible given a fixed amount of storage capacity at each consumer

## Slide 101: Under-utilization of Spatial tiling
Under-utilization when
  M< Number of PEs in a column or N <Number of PEs in a row
    M: number of output channels
    N: number of input channels
Solution
  Multiple tiles of data run at the same time
  Sufficient flexibility of data delivery and the NoC
    Provide sufficient bandwidth

## Slide 102: PE with Memory Access

## Slide 103: DRAM Access
Worse Case: all memory R/W are DRAM accesses

## Slide 104: Leverage Local Memory for Data Reuse
Temporal reuse: the same data is used more than once over time by the same consumer

## Slide 105: Hierarchical Blocking of a Single Convolutional Layer

## Slide 106: Formal Derivation of CONV
Loop representation string
  Rules for each new character
  Buffer
  Re-fetch rate

## Slide 107: Recursive Formulation
Fixed order as follows
__
From left to right observing
Buffer Refetch Rate: the number of times a piece of data is fetched from a certain buffer after initially being loaded into that buffer

## Slide 108: Recursive Formulation
Fixed order as follows
__
From left to right observing
  X or Y: new KB
Buffer Refetch Rate: the number of times a piece of data is fetched from a certain buffer after initially being loaded into that buffer

## Slide 109: Recursive Formulation
Fixed order as follows
___
From left to right observing
  X or Y: new KB
  C: new OB
Buffer Refetch Rate: the number of times a piece of data is fetched from a certain buffer after initially being loaded into that buffer

## Slide 110: Recursive Formulation
Fixed order as follows
___
From left to right observing
  X or Y: new KB
  C: new OB
  K: new IB
Buffer Refetch Rate: the number of times a piece of data is fetched from a certain buffer after initially being loaded into that buffer

## Slide 111: How Does Parallelism Work?
Unroll Loops in Space
Replicate Compute Units
Perform Loops in parallel
  SIMD
  Multiple Cores
  Multiple CPU/GPUs

## Slide 112: Multi-Core Parallelism and Partitioning
Across channels (C)
  Reduction
  Synchronization
Across kernels (K)
  Synchronization
Across image (X or Y)
  Independent
Broadcast operation
Partitioned memory
Nested parallelism

## Slide 113: High Performance Direct Convolution
Map application to system architecture to fully exploit system capacity

## Slide 114: High Performance Direct Convolution
Analytical model to achieve system theoretical peak performance

## Slide 115: Better Performance

## Slide 116: Types of Data Reuse in DNN
If all data reuse is exploited, DRAM accesses in AlexNet
can be reduced from 2896M to 61M (best case)

## Slide 117: Parallelism: Parallel MAC Units

## Slide 118: Parallelism: Spatial Data Reuse
Spatial reuse: the same data is used by more than one consumer at different spatial locations of the hardware.

## Slide 119: Spatial Architecture for DNN

## Slide 120: Multi-Level Low-Cost Data Access
A Dataflow is required to maximally exploit data reuse with the low-cost memory hierarchy and parallelism

## Slide 121: Recap CNN Decoder Ring

## Slide 122: Dataflow and Loop Nest
No ordering or notion of parallelism on the individual calculations
  But are important for Hardware for performance and efficiency computation
Dataflow
  Specifying an ordering and which calculation run in parallel
  Computation order
  Data movement order
Loop Nest
  Describe Various properties of a given DNN accelerator design
  Describe Dataflow
  for: temporal for, describes the temporal execution order
  spatial_for: describes parallel execution

## Slide 123: Data Reuse in DNN
Total # of MACs:
  RSCEFM
Input Activation
  Size: HWC
  Reuse:~RSM
Weight
  Size: RSCM
  Reuse: EF
Output Activation
  Size: EFM
  Reuse: RSC

## Slide 124: 1D Convolution Example
Weight Stationary
(WS) Dataflow
Output Stationary
(OS) Dataflow
Input Stationary
(IS) Dataflow

## Slide 125: Single Processing Engine(PE) Setup

## Slide 126: Output Stationary – Reference Pattern

## Slide 127: Output Stationary – Reference Pattern
Single output is reused many times (R)

## Slide 128: Output Stationary – Reference Pattern
Single output is reused many times (R)
All weights reused repeatedly

## Slide 129: Output Stationary – Reference Pattern
Single output is reused many times (R)
All weights reused repeatedly
Sliding window of inputs (size = R)

## Slide 130: Buffer Access Pattern (OS)

## Slide 131: Buffer Data Accesses

## Slide 132: Buffer Data Accesses

## Slide 133: Buffer Data Accesses

## Slide 134: Weight Stationary – Reference Pattern

## Slide 135: Weight Stationary – Reference Pattern
Single weight is reused many times (E)
Large sliding window of inputs (size = E)
Fixed window of outputs (size = E)

## Slide 136: Buffer Access Pattern (WS)

## Slide 137: L1 Weight Stationary - Costs
 | OS | WS | IS | Min
MACs | E*R | E*R |  | 
Weight Reads | E*R | R |  | 
Input Reads | E*R | E*R |  | 
Output Reads | 0 | E*R |  | 
Output Writes | E | E*R |  | 

## Slide 138: Tiled Loop Nest For Weight-stationary

## Slide 139: Parallel Processing for The A Tile Of Filter Weights

## Slide 140: Reference Pattern for Parallel Processing
R = 4
E = 9
W = 12
R1 = 2
R0 = 2

## Slide 141: Weight Stationary Dataflow
Original nested loop:

## Slide 142: Weight Stationary Dataflow
Change temporal ordering

## Slide 143: Weight Stationary Dataflow
Apply spatial parallelism

## Slide 144: Weight Stationary Dataflow
Apply temporal tiling (NVDLA Dataflow (nvdla.org))

## Slide 145: Input Stationary – Reference Pattern
Implement input stationary with no input index
Beware w - r must be >= 0 and <E

## Slide 146: Input Stationary – Reference Pattern
Inputs used repeatedly (R times)
Weights reused in large window (size = R)
Sliding window of outputs (size = R)

## Slide 147: Buffer Access Pattern (OS)

## Slide 148: Minimum Costs
 | OS | WS | IS | Min
MACs | E*R | E*R | E*R | E*R
Weight Reads | E*R | R | E*R | R
Input Reads | E*R | E*R | E | E
Output Reads | 0 | E*R | E*R | 0
Output Writes | E | E*R | E*R | E
Assume: W ~= E

## Slide 149: Intermediate Buffering

## Slide 150: 1-D Convolution – Buffered
Note E and R are factored so:
E0*E1 = E
R0*R1 = R

## Slide 151: Buffer Sizes
Level 0 buffer size is volume needed in each Level 1 iteration
Level 1 buffer size is volume needed to be preserved and redelivered in future (usually successive) Level 1 iterations
A legal assignment of loop limits will fit into the hardware’s buffer sizes

## Slide 152: Spatial PEs

## Slide 153: 1-D Convolution – Spatial
Note:
E0*E1 = E
R0*R1 = R
R0*E0 <= #PEs

## Slide 154: Outline
Benchmarking Metrics
GEMM Accelerator Design
DNN Accelerator Design
  Locality and Data Reuse
  Dataflow Taxonomy
  Network-on-Chip
  Optimization
Energy

## Slide 155: Dataflow Taxonomy
Minimizing data movement is the key to achieving high energy efficiency for DNN accelerators
Dataflow taxonomy:
  Output Stationary: minimize movement of psums
  Weight Stationary: minimize movement of weights
  Input Stationary: minimize movement of inputs
Loop nest provides a compact way to describe various properties of a dataflow, e.g., data tiling in multi-level storage and spatial processing.

## Slide 156: Dataflow Taxonomy

## Slide 157: Output Stationary (OS)
Minimize partial sum R/W energy consumption
  Maximize local accumulation
Broadcast/Multicast filter weights and reuse
  Activations spatially across the PE array

## Slide 158: OS Example: ShiDianNao

## Slide 159: OS Example: ENVISION

## Slide 160: Variations of Output Stationary

## Slide 161: Output Stationary Dataflow
Cycle through input fmap and weights (hold psum of output fmap)

## Slide 162: Output Stationary Dataflow
Cycle through input fmap and weights (hold psum of output fmap)

## Slide 163: Output Stationary Dataflow
Cycle through input fmap and weights (hold psum of output fmap)

## Slide 164: Output Stationary Dataflow
Cycle through input fmap and weights (hold psum of output fmap)

## Slide 165: Weight Stationary (WS)
Minimize weight read energy consumption
  Maximize convolutional and filter reuse of weights
Broadcast activations and accumulate psums
  Spatially across the PE array.

## Slide 166: WS Example: nn-X (NeuFlow)

## Slide 167: WS Example: NVDLA (Simplified)

## Slide 168: WS Example: NVDLA (Simplified)

## Slide 169: Loop Nest For Simplified NVDLA

## Slide 170: Weight Stationary Dataflow
Cycle through input and output fmap (hold weights)

## Slide 171: Weight Stationary Dataflow
Cycle through input and output fmap (hold weights)

## Slide 172: Weight Stationary Dataflow
Cycle through input and output fmap (hold weights)

## Slide 173: Weight Stationary Dataflow
Load new weights

## Slide 174: Weight Stationary Dataflow
Cycle through input and output fmap (hold weights)

## Slide 175: Input Stationary (IS)
Minimize activation read energy consumption
  Maximize convolutional and fmap reuse of activations
Unicast weights and accumulate psums spatially
  Across the PE array.
Usually for sparse CNNs

## Slide 176: IS Example: SCNN
Used for sparse CNNs
  Sparse CNN is where many weights are zeros
  Activations also have sparsity from ReLU

## Slide 177: Eyeriss - Row Stationary (RW)
Maximize data reuse at Register File
  Maximize row convolutional reuse in Register File
    Keep a filter row and fmap sliding window in Register File
  Maximize row psum accumulation in Register File
Optimize for overall energy efficiency instead for only a certain data type

## Slide 178: 1D Row Convolution in PE

## Slide 179: 1D Row Convolution in PE

## Slide 180: 1D Row Convolution in PE

## Slide 181: 1D Row Convolution in PE

## Slide 182: 2D Convolution in PE Array

## Slide 183: 2D Convolution in PE Array

## Slide 184: 2D Convolution in PE Array

## Slide 185: 2D Convolution in PE Array

## Slide 186: Convolutional Reuse Maximized
Filter rows are reused across PEs horizontally

## Slide 187: Convolutional Reuse Maximized
Fmap rows are reused across PEs diagonally

## Slide 188: Maximize 2D Accumulation in PE Array
Partial sums accumulate across PEs vertically

## Slide 189: Dimensions Beyond 2D Convolution
Multiple Fmaps
Multiple Filters
Multiple Channels

## Slide 190: Multiple Filters - Fmap Reuse in PE
Processing in PE: interleave filter rows

## Slide 191: Multiple Filters - Fmap Reuse in PE
Processing in PE: interleave filter rows

## Slide 192: Multiple Channels - Channel Accumulation in PE
Processing in PE: interleave filter rows

## Slide 193: The Full Picture
Map rows from multiple fmaps, filters and channels to same PE to exploit other
forms of reuse and local accumulation

## Slide 194: Eyeriss DNN accelerator

## Slide 195: Taxonomy: More Examples

## Slide 196: Outline
Benchmarking Metrics
GEMM Accelerator Design
DNN Accelerator Design
  Locality and Data Reuse
  Dataflow Taxonomy
  Network-on-Chip
  Optimization
Energy

## Slide 197: A Common Design Pattern

## Slide 198: A Common Design Pattern
PE array underutilized If there are fewer input and/or output channels than the array dimensions
Effective data delivery BW also becomes lower → further impact performance
Not scalable → utilization will be worse at larger scales

## Slide 199: A More Flexible Data Delivery Strategy
Adapt to the reuse and bandwidth requirements

## Slide 200: Common NoC Design

## Slide 201: Common NoC Designs on DNNs

## Slide 202: Spatial Accumulation DNN Accelerator Design
Input activations (Iacts) are reused vertically
Partial sums are accumulated horizontally
Often used for a weight-stationary dataflow

## Slide 203: Temporal Accumulation DNN Accelerator Design
Input activations (Iacts) are reused vertically
Weights are accumulated horizontally
Often used for an output-stationary dataflow

## Slide 204: Mesh Network – Best of Both Worlds

## Slide 205: Mesh Network – More Complicated Cases

## Slide 206: Hierarchical Mesh Network
Flexible to support patterns ranging from high reuse to high bandwidth scenarios
Can be easily scaled at a low cost

## Slide 207: Different Operating Modes

## Slide 208: Different Operating Modes

## Slide 209: Scaling the Hierarchical Mesh Network

## Slide 210: Hierarchical Mesh Networks CONV Layer
Keep all four PE the lowest bandwidth requirement
  2 input activations
  2 weight
HM-NoC Configurations (2 options)
  Grouped-multicast for input activations Interleaved-multicast for weights
  Grouped-multicast for weights Interleaved-multicast for input activations

## Slide 211: Hierarchical Mesh Networks Depth-wise CONV Layer
Nearly no reuse for input activation
Exploit the reuse of weights
HM-NoC Configurations
  Broadcasting the weights to all Pes
  Fetching unique input activation for each PE

## Slide 212: Hierarchical Mesh Networks Depth-wise CONV Layer
Little reuse for weights
  Especially when the batch size is limited
HM-NoC Configurations
  Weights are now unicast to the Pes
  Input activations are broadcast to all Pes

## Slide 213: Eyeriss with Hierarchical Mesh Network

## Slide 214: Outline
Benchmarking Metrics
GEMM Accelerator Design
DNN Accelerator Design
  Locality and Data Reuse
  Dataflow Taxonomy
  Network-on-Chip
  Optimization
Energy

## Slide 215: Datapath Optimization
spatial_for - to explore parallelism
  Spatial-K: accumulation dimension
    Adder tree/dot product
    Systolic accumulation
  Spatial-M/N: data reuse dimension
    Direct-wiring multicast
    Systolic multicast
State-of-the-art accelerators typically use a combination of both at different levels of the hierarchy.

## Slide 216: Matrix Multiply

## Slide 217: Datapath Optimization - Spatial-K
Type 1: Adder Tree
Example: NVDLA, DianNao
Typical width: 8-64
Applicable to any accumulation dimensions
  E.g., R, S, C in convolution

## Slide 218: Datapath Optimization - Spatial-K
Type 2: Systolic Accumulation
Example: TPU, Gemmini
Typical width: 8-256
Applicable to any accumulation dimensions
  E.g., R, S, C in convolution

## Slide 219: Datapath Optimization - Spatial-N
Type 1: Direct-wiring multicast
Example: NVDLA, DianNao
Typical width: 8-16
Applicable to any non-accumulation dimensions

## Slide 220: Datapath Optimization - Spatial-N
Type 2: Systolic multicast
Example: TPU, Gemmini
Typical width: 8-256
Applicable to any non-accumulation dimensions

## Slide 221: Datapath Optimization Combined: NVDLA
Adder-tree accumulation
Direct-wiring multicast

## Slide 222: Datapath Optimization - Spatial-K
Systolic accumulation
Systolic multicast

## Slide 223: Memory Optimization
Short-lived intermediate results
Instead of accessing SRAM or a shared, large register file
  Consume the intermediate results directly
Example: adder tree and systolic accumulation

## Slide 224: Memory Optimization
App-specific storage size/BW
Dedicated storage for each operand
NVDLA
TPU

## Slide 225: Memory Optimization
App-specific data delivery
Double-buffering
  Goal: Overlap compute and communication by doubling the SRAM sizes.
  Producer writes to a buffer while Consumer reads from the other buffer

## Slide 226: Memory Optimization
App-specific data delivery
Double-buffering
  Goal: Overlap compute and communication by doubling the SRAM sizes.
  Producer writes to a buffer while Consumer reads from the other buffer

## Slide 227: Tensor Processing Unit
Datapath:
  Spatial-K: Systolic Accumulation
    Multi-cycle with registers
  Spatial-N: Systolic multicast
    Multi-cycle with registers
  Better scalability
Memory
  Custom systolic registers
  Dedicated accumulation and weight buffers
  Double-buffered, weight-stationary dataflow
TPU

## Slide 228: Outline
Benchmarking Metrics
GEMM Accelerator Design
DNN Accelerator Design
Energy

## Slide 229: Don’t Forge Memory System Energy

## Slide 230: Don’t Forget Cache Energy
Energy with Corrected Cache Size

## Slide 231: Dark Silicon View
Efficient Accelerators
Increase Chip’s
  Energy Efficiency
  Area Efficiency
Report 10~1000x improvements

## Slide 232: Real Perspectives
Efficient Accelerators
Increase Chip’s
  Energy Efficiency
  Area Efficiency
Report 10~1000x improvements
Inefficient System
Efficient Chip

## Slide 233: Dark Memory Perspectives
Efficient System
On-chip buffers
  Less efficient chip
Lower Off-chip Memory Bandwidth
Efficient System
Locality

## Slide 234: Dark Memory
Keep DRAM and Memory Hierarchy Dark
First Focus on Memory Hierarchy
Algorithm: minimize DRAM access
High chip level locality when parallelized

## Slide 235: Metrics for Resource Constrained Computing
Data Parallel Space
More Performance
More Hardware
More Power
More Area

## Slide 236: Scale by Performance
Energy/OP
Area/OP
One Pareto Optimal
Diming the chip

## Slide 237: Always (FL)OPs?
Define op
  Invariant across the different implementations
DFT and FFT
  Op is one Transform
(Convolutional) Neural Networks
  Op is one Inference
Dense and Sparse Solvers
  Op is a number of solutions

## Slide 238: System Design Optimization
Sensitivity study along the Pareto Curves (Puzzle)
Trade Area/Performance of one IP with another
Both Scalable and Non-scalable

## Slide 239: Example: Blocked GEMM
A or B
  From a x a buffer
  N3 / a
C
  Access for last level cache is 2N2
Highest level always suffers from constant N3 accesses to A and B

## Slide 240: One Level Caching DP-FP

## Slide 241: The Energy vs. Size of Top Level
Energy Consumption
  Boosts significantly as size grows
Memory Size:
  Does not compensate for the access savings

## Slide 242: Let’s Add Another Layer
A or B
  From b x b buffer
  N3 / b
C
  Access for last level cache is 2N2

## Slide 243: Second-level Caching

## Slide 244: Three Levels

## Slide 245: Memory Subsystem = Half Energy

## Slide 246: Putting It All Together
Merging FPU Pareto with Memory Pareto

## Slide 247: Algorithm/Architecture Co-design Methodology